## Slide 1
TRIDENT OPS
EVIDENCE-FIRST PREDICTIVE MAINTENANCE + OEE
Team Name: TRidents
Team Leader: Ashok Jangam
Team Size: 4
Problem Statement: Predictive Maintenance and OEE Command Center
Two evidence lanes. One auditable decision path. Zero fabricated joins.

## Slide 2
01 · PROBLEM BRIEF
The gap isn't a model. It's a missing thread.
PIADE
Real line states alarms + package counts weighted OEE
MetroPT
Real compressor sensors + failure windows no production counts
NO-JOIN FIREWALL
different plants · no shared key
The honest product
PIADE drives OEE, ownership and next-hour ranking. MetroPT remains a separate sensor-evidence lane labelled detection—not forecast.
Sources: PIADE DOI 10.5281/zenodo.7071747 · MetroPT-3 DOI 10.24432/C5VW3R · both public

## Slide 3
02 · ARCHITECTURE
One console. Two databases. Three working tines.
PIADE CSV
states · alarms · counts
SNOWCORE_REAL
BRONZE → SILVER → GOLD → ML
MetroPT
pressure · current · load
PNEUMORA
CORE → ML → evidence
TRIDENT OPS
COMPUTE
OEE + baseline
EXPLAIN
bounded Cortex
ACT
idempotent row
TRIDENT_OPS.OPS.TRIAGE_ACTION
Snowflake: warehouse Streamlit · Snowpark SQL procedures · AI_COMPLETE · governed views

## Slide 4
03 · MEASURED IMPACT
Evidence before ego
46.78%
PIADE weighted OEE
A 64.32% × P 72.93% × Q 99.72%
76.4%
Blind top-decile precision
Persistence baseline 62.4%; archived Dec-2021 holdout
+72 / +86
MetroPT external timing
minutes after leak onset · NO PROMOTION
What changed because of the model?
Not yet measured. OEE lift and realised savings require intervention data.
What did automation prove?
45 replay orders · 35.6% hit rate · 1.26× random timing · 23% coverage
What did search teach us?
25 trials improved validation AUC by 0.0001. Missing signal—not another model—is the ceiling.
Every number is Observed, Derived, Model, Scenario or Operator-entered · no unlabelled financial claim

## Slide 5
04 · END-TO-END COCO CLI WORKFLOW
The 4-minute proof: compute → explain → act
1
COMPUTE
CoCo queries weighted OEE and ownership. Streamlit shows the same deterministic row.
2
EXPLAIN
Five alarm-pattern rows go to Cortex. The answer cites codes and states what is unknown.
3
ACT
The operator opens an inspection. A Snowflake MERGE writes one reload-safe action.
BLACK-BOX RESULT
same input → same action id → second run deduplicated=true
Saved prompts: docs/demo/01_oee.txt · 02_rca.txt · 03_action.txt

## Slide 6
LIVE TRIDENT OPS CODE github.com/ashokjangam/snowcore-pdm
Compute. Explain. Act. Admit what the evidence cannot prove.