## Slide 1
PNEUMORA
EARLY AIR-LEAK PREDICTION ON REAL COMPRESSOR SENSORS
Team Name: TRidents
Team Leader: Ashok Jangam
Team Size: 4
Problem Statement: Predictive Maintenance and OEE Command Center
Nine real failures. Three compressors. A breakdown predicted hours ahead.

## Slide 2
01 · PROBLEM BRIEF
A leaking compressor takes a train out of service.
REAL
MetroPT sensors pressure · current oil temp · load
LABELLED
synthetic work orders parts · crew example-factory OEE
EXISTING ALARM
3 of 7
air leaks flagged ≥ 2 h before removal 0.49 false alerts per healthy day
Same asset, one thread
PNEUMORA reads the compressor’s real sensor streams, predicts 6 of 7 air-leak breakdowns hours ahead with about a ninth of the alarm’s false alerts, and turns each one into a cited, recorded maintenance decision.
Sources: MetroPT-3 DOI 10.24432/C5VW3R · MetroPT 2022 Zenodo 6854240 · MetroPT-2 Zenodo 7766691 · 9 documented failures

## Slide 3
02 · ARCHITECTURE
Raw sensor cycles in. A recorded decision out.
MetroPT raw
1 Hz / 10 s · 3 units
CORE + ML
cycle physics · 5-min telemetry ANOMALY_DETECTION
Synthetic CMMS
labelled, same asset
OPS
work orders · parts · crew ACTION_LOG
PNEUMORA app
PREDICT
leak physics + native ML
EXPLAIN
AI_COMPLETE, typed + cited
ACT
idempotent MERGE
PNEUMORA.OPS.RECORD_ACTION
Snowflake: warehouse-runtime Streamlit · SNOWFLAKE.ML.ANOMALY_DETECTION · Cortex AI_COMPLETE · SQL procedure · isolated PNEUMORA database

## Slide 4
03 · MEASURED RESULTS
It predicts the breakdown hours ahead. Promoted.
6 of 7
Air leaks predicted ≥ 2 h ahead
Held out by compressor · existing alarm 3 of 7 · 0.056 vs 0.49 false alerts/day
5.8 h
Median warning before removal
PROMOTED_CROSS_VALIDATED · all five pre-declared gates passed · chance p = 3e-7
1 of 9
Warned before the leak began
Leaks start abruptly · best of six approaches · it predicts the breakdown, not the leak
Snowflake native ML + gradual leaks
ANOMALY_DETECTION: 4 of 4 in time. Injected 2× air-loss leak caught 28 of 30 (control 7).
What we generated
Replayed onsets and physics-injected leaks, all SYNTHETIC_TRAINING_ONLY, never used to score.
Caveats we show on screen
Protocol v2 written after v1 failed on false alerts; no untouched data left. No oil leaks, RUL or savings.
Predicted = alert from 2 h before leak start to 2 h before reported end (dataset owners’ protocol) · settings chosen on the other two compressors

## Slide 5
04 · END-TO-END COCO CLI WORKFLOW
The 4-minute proof: predict → explain → act
1
PREDICT
CoCo reads failures, alerts and native-ML results. The app shows the held-out prediction record.
2
EXPLAIN
Observed F04 facts go to Cortex. Every number cites its field; no invented parts.
3
ACT
The crew opens an inspection. A Snowflake MERGE writes one reload-safe row.
BLACK-BOX RESULT
same decision → same action id → second call deduplicated=true
Saved prompts: docs/demo/01_detect.txt · 02_rca.txt · 03_action.txt

## Slide 6
LIVE PNEUMORA CODE github.com/ashokjangam/snowcore-pdm
Predict the breakdown. Explain with evidence. Record the decision. Say where prediction ends.